## Slide 1: Development of novel SFC/MS methods for the analysis of metabolites
RNDr. Oleksandr Kozlov, PhD.

## Slide 2: Aim of postdoctoral project
The aim of the postdoctoral project is the development of new supercritical fluid chromatography (UHPSFC) coupled to mass spectrometry (MS) methods for the analysis of both lipophilic and hydrophilic metabolites in biological samples.

## Slide 3: SFC/MS analysis of lipids
SFC usually employs CO2-based mobile phases with certain portions (1–50%, v/v) of a polar organic co-solvent (methanol, isopropanol).
Ultrahigh-performance SFC – using of columns with sub–2 μm particles.
Lipids are a wide group of important metabolites that are involved in a wide range of functions in living organisms.
Lipid species can be used as biomarkers of serious diseases, including cancer.
Mass spectrometry (MS) is a key analytical technique for the detection and identification of lipids.

## Slide 4: 1. UHPSFC intraclass separation of lipids
Peak annotation:
CE – cholesteryl esters;
DG – diacylglycerols;
TG – triacylglycerols;
Cer – ceramides;
HexCer – hexosylceramides;
PE – phosphatidylethanolamines;
PC – phosphatidylcholines;
SM – sphingomyelins;
LPC – lysophosphatidylcholines.

## Slide 5: 1. UHPSFC intraclass separation of lipids
The effects of mobile phase composition and gradient, flow rate, back pressure, temperature, and column coupling were evaluated in detail.
Influence of temperature:
Column coupling:

## Slide 6: 1. UHPSFC intraclass separation of lipids
Conclusions:
UHPSFC intraclass separation of lipids was achieved according to the acyl chain composition together with preserved interclass selectivity.
The nature of the stationary phase was the main factor influencing intraclass separations of lipids.
The Torus Diol and Torus 1-AA columns showed the best results.
The column temperature and column
coupling had the prominent effect on
the separation of lipids.
Separation of selected
regioisomers and isobaric species
was achieved in some cases.

## Slide 7
2. Chiral SFC separation of MG and DG
Monoacylglycerols (MG) and diacylglycerols (DG) are important in a wide range of metabolic pathways; signaling molecules
Emulsifiers in the pharmaceutical, food and cosmetics industries
Enantiomeric MG and DG are potential precursors for the synthesis of lipids

## Slide 8
2. Chiral SFC separation of MG and DG
Synthesis of MG and DG enantiomers using the 7 most commonly occurring fatty acids in biological samples such as palmitic, stearic, oleic, linoleic, linolenic, arachidonic, and docosahexaenoic acids was performed.
Chiral SFC/MS method development
Column chemistry, mobile phase composition and gradient, flow rate,
backpressure, and temperature were carefully assessed.
Lipase-catalyzed hydrolysis of triacylglycerols
The developed method was used for the analysis of hydrolysis products of triacylglycerols and to evaluate selectivity of lipases from porcine pancreas and Pseudomonas fluorescens.

## Slide 9
2. Chiral SFC separation of MG and DG
Conclusions:
The baseline separation of all MG and DG in 5 min under the optimized conditions was achieved.
The most prominent effects of stationary phase and mobile phase modifier types on the enantioseparation was confirmed.
The different stereoselectivities of lipases were observed, which strongly depended on the type of prochiral substrate.

## Slide 10
3. SFC-MS analysis of MG and DG enantiomers: selectivity modulation
Coelution of MG and DG with highly abundant triacylglycerols (TG) in biological samples
MS response may be affected due to ion suppression effects inaccurate quantification
Solution:
Coupling of achiral and chiral columns, modulation of acylglycerol selectivity

## Slide 11
3. SFC-MS analysis of MG and DG enantiomers: selectivity modulation
Single amylose-based
chiral columns
Coupling of chiral and achiral (C18) columns

## Slide 12
3. SFC-MS analysis of MG and DG enantiomers in biological samples
Chiral SFC-MS analysis of egg yolk, human plasma, and porcine brain samples showed different ratios of enantiomers, suggesting their unique roles within each
sample type.

## Slide 13
4. SFC-MS lipidomic/metabolomic analysis
Proof of concept for the application of a commercial SFC-MS instrument for the comprehensive analysis of metabolites with the full range of polarities was demonstrated.
The developed single-platform SFC−MS lipidomic/metabolomic method is based on two consecutive injections of lipid and polar metabolite extracts from biphase methyl tert-butyl ether extraction.

## Slide 14
4. SFC-MS lipidomic/metabolomic analysis
Fast and comprehensive SFC-MS analysis of lipids and polar metabolites from plasma was performed from the same vial by adjustment of the needle placement using a simple analytical platform based on a single instrument, column, and mobile phase.